## Slide 1: 4CS015 Fundamentals of Computing
1

## Slide 2: A. Agenda
Introduction to your Instructors
Introduction to the Module
Week 1 Lecture on Fundamentals of Computing
Agenda
Instructors
2

## Slide 3: B. Instructors
Uttam Acharya (Module Leader)
  MSc. Physics, TU
    uttam.acharya@heraldcollege.edu.np
Sanjeev Rai (Lecturer)
  MCA (Masters of Computer Application), PU
    sanjeev.chamling@bicnepal.edu.np
Bhismaraj Koirala (Tutor )
  BE(Bachelor of Computer Engineering),TU
Sandhya Tiwari (Tutor )
  BIM(Bachelor of Information Management),TU
Agenda
Instructors
Module Overview
3
Agenda
Instructors

## Slide 4: C. Module Overview
Week 1: Number and Data representation
Week 2: Digital Electronics
Week 3: Combinational Circuits
Week 4: Arithmetic Logic Units
Week 5: Sequential logic
Week 6: Memory
Week 7: CPU Architecture and Peripheral Devices
Week 8: Windows Operating System and Command line Interface
Week 9: Exam Week
Week 10: Linux Operating system and Command line
Week 11: Batch file for Windows OS
Week 12: Networking and Final Portfolio Submission
Instructors
Module Overview
Teaching Strategy
4

## Slide 5: C. Module Overview
This module has two distinct halves.
Weeks 1 – 6
The first half looks at the relationships between number systems, Boolean algebra, logic gates and digital electronic circuit design.
By the end, you should have a good understanding of how a computer works and why it works that way.
Weeks 7 – 12
The second half examines how Computer Scientists get the most out of computers.
You’ll look at how we work with computers that don’t have ‘point and click’ front ends, how we communicate with other computers and how to store and access data.
Instructors
Module Overview
Teaching Strategy
5

## Slide 6: D. Teaching Strategy
Taught over 1 Semester – 12 Weeks
  Each Week Consists of:
    1 Lecture: 2 hrs => Discuss the conceptual idea of the topic
    1 Tutorial:2 hrs =>Discuss to clear confusions
    1 Workshop 2.5 hrs =>Practice the concept and ideas
Module Overview
Teaching Strategy
Recommended
Textbooks
6

## Slide 7: E. Recommended Textbooks:
rd
Computer System Architecture
  M. Morris Mano (Pearson, 3 Edition )
Logic and Computer Design Fundamentals
  M. Morris Mano and C.R. Cime (Pearson,2008)
Teaching Strategy
Recommended
Textbooks
Module grading system in UK
7

## Slide 8: F. Module grading system in UK
8
Recommended Textbooks
Module grading
system in UK
Any Questions?

## Slide 9: Weekly Study Hour
Credits Hours Breakdown
Each of your module carries 20 Credits
Total Learning Time: 20 Credits x 10 hrs= 200 hrs. (Since 1 Credit = 10 Hours of Learning Hours)
Guided Learning (Comprises of LTW sessions):
35% of Total Learning Hours (200 hrs.) = 70 Hours
Unguided Learning (Comprises of self-studies and time taken for the assessments):
65% of Total Learning Hours (200 hrs.) = 130 Hours
9
G. Classroom Code
H. Weekly Study our
1. Lecture 1

## Slide 10: Lecture-1 Number and Data Representation

## Slide 11: 2. Overview
Representation of Numbers
Base/Radix:
Decimal
Binary
Octal
Hexadecimal
Unsigned and Signed numbers
Two’s Complement Subtraction
Non-integer numbers
1. Lecture- 1
2. Overview
2.1 Some Definitions

## Slide 12: 2.1 Some Definitions
12
2.1.1 Analogue
Pic Ref: bbc.co.uk
  Some Definitions
    Analogue
    Digital
Continuous signals
Represented by sine waves
Human voice, sound, light are a few examples

## Slide 13: 2.1.2 Digital –
13
Pic Ref: answers.com
  Some Definitions
    Analogue
    Digital
Discrete signals
Represented by square waves
For example, electricity

## Slide 14: 2.1.3 Digital Electronics
14
Digital electronics takes different values (or ranges of values) of analogue signals to represent different, discrete, values.
As an example, consider a light switch A light switch only has two positions.
When it is ‘off’, we would measure 0 volts at the supply to the light.
When it is ‘on’, we would measure 240 volts at the supply to the light.
Thus, we can represent ‘on’ and ‘off’, or ‘0’ and ‘1’, with two arbitrary analogue values; ‘0’ and ‘240’ (In the USA,
they use ‘0’ and ‘110’).
  Some Definitions
    Analogue
    Digital
    Digital Electronics

## Slide 15: 2.2 Representation
All information when stored in a computer system, must use some form of internal representation
The program to be executed.
The numerical data to be processed.
Character strings ( A....Z etc. ).
2.2 Representation
15
2.3 Radix or Base

## Slide 16: 2.3 RADIX or BASE
16
In any number scheme the base value defines the number of unique symbols. In the Decimal scheme we use the symbols: 0,1,2,3,4,5,6,7,8,9.
The highest symbol = BASE –1.
All Symbol values are UNIQUE.
Example: 1110
  2.4The Decimal
System
2.5 Binary
2.3 RADIX or BASE

## Slide 17: 2.3 The Decimal System
What is a Decimal Value?
What does 331 really mean?
The position of each digit is assigned a weight.
Decimal Scheme right-most digit has a weight of 100 = 1.
Weighting increases by a factor of 10 for each new symbol as the position moves to the left.
2.3 The Decimal
17
System
2.3.1 Decimal
Example

## Slide 18: 2.3.1 Decimal Example
18
Again taking the value 331:
Value = 300 + 30 +1.
102 | 101 | 100
3 | 3 | 1
3 * 100 | 3 * 10 | 1 * 1
300 | 30 | 1
  2.3 The Decimal
System
    2.3.1 Decimal Example
  2.4 The Binary

## Slide 19: 2.4 Binary
Binary number system follows similar rules to decimal system.
Except base is 2 not 10.
By the BASE rules:
Symbols: 0, 1 (all symbols are unique) Highest Symbol = BASE - 1.
BASE = 2 this is BINARY.
Example: 112
19
  2.3.1 Decimal example
2.4 Binary

## Slide 20: 3. The Binary Representation Scheme
Can you tell what this value is?
20
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
Taking a simple value: 01011010
The Binary Representation Scheme
  Basic Conversion
  Decimal to Binary Conversion

## Slide 21: 3.1 Basic Conversion
Converting this representation back to a more familiar DECIMAL form we can see that all the information necessary about the data is available.
0 + 64 + 0 + 16 + 8 + 0 + 2 + 0 = 90
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0*128 | 1*64 | 0*32 | 1*16 | 1*8 | 0*4 | 1*2 | 0*1
3. The Binary
21
Representation Scheme
3.1 Basic Conversion
3.2 Decimal to Binary Conversion

## Slide 22: 3.2 Decimal To Binary Conversion
22
Rules:
  Divide the number by 2.
  Look at the remainder ‘1’ or ‘0’.
  Use the remainder as Bit value.
  Loop till done.
Convert 2510
3. The Binary
Representation Scheme
3.1 Basic Conversion
3.2 Decimal to Binary
Conversion

## Slide 23: 3.2.1 Example: Conversion of 2510
Binary Value = 110012
Divisor | Quotient | Remainder
2 | 25 | 1 LSB
2 | 12 | 0
2 | 6 | 0
2 | 3 | 1
2 | 1 | 1 MSB
 | 0 | 
  Decimal to Binary Conversion
    Example

## Slide 24: 3.3 Binary To Decimal Conversion
Calculate the value for each Digit Position as (Symbol * Base Weighting) for the position. Then sum all these values.
  Binary 11102
= (1 * 23) + (1 * 22) + (1 * 21) + (0 * 20)
= (1 * 8) + (1 * 4) + (1 * 2) + (0 * 1)
= 1410
3.3 Binary to Decimal
Conversion
3.4 Most Significant
Digit /
Least Significant Digit
4. 'Bits', 'Bytes' and
'Words'

## Slide 25: 3.4 Most Significant Digit / Least Significant Digit
The concepts of the significance of the Symbol positions is not unique to binary.
  Units, Tens, Hundreds etc. In the decimal scheme.
Most Significant Digit is the Left - most symbol of the Number.
Least Significant Digit is the Right – most symbol of the Number.
Example: 110012
3.3 Binary to Decimal
Conversion
3.4 Most Significant
Digit /
Least Significant Digit
4. 'Bits', 'Bytes' and
'Words'

## Slide 26: 4. 'Bits', 'Bytes' and 'Words'
Within a computer system EVERYTHING is stored or used in binary format.
Each Binary Digit is commonly known as a
Bit.
Within any computer system information is stored or manipulated in groups of ‘n Bits’.
3.4 Most Significant
Digit /
Least Significant Digit
4. 'Bits', 'Bytes' and
'Words’
5.Unsigned Numbers

## Slide 27: 4. 'Bits', 'Bytes' and 'Words'
A Byte is the smallest grouping and it is defined to contain ‘n’ Bits. By common usage, the Byte usually refers to a grouping of 8 Bits.
A Word is a larger grouping of Bits.
Size reflected by a PC’s architecture.
Again by common usage, a Word is a grouping of 16 Bits
and therefore is 2 Bytes.
We also have Nibbles
  Which are?
3.4 Most Significant
Digit /
Least Significant Digit
4. 'Bits', 'Bytes' and
'Words’
5.Unsigned Numbers

## Slide 28: 5.Unsigned Numbers
Any number range is defined as:
  0 Max Number.
In the Decimal scheme, if we write a value as 27:
  The magnitude of the value is 27.
  By convention the value is Positive.
On the other hand if we write the value as: -27
  It is not the same since the '-' SIGN identifies it as another value.
4. 'Bits', 'Bytes' and
'Words’
5.Unsigned Numbers

## Slide 29: 5.1 Unsigned Binary Representation
The Binary representation in an unsigned form has only a MAGNITUDE.
All binary combinations of the "n" Bits will uniquely identify a magnitude
e.g. 0000 1111.
Range 0 to 2n -1
So program variable declarations can define the size and type of storage used!
5.Unsigned Numbers
5.1 Unsigned Binary
Representation
5.2 Kilo-Mega-Giga
5.3 Unsigned Number
Tables

## Slide 30
5.2 Kilo - Mega - Giga
Within Binary these terms have slightly different
meaning to those in Decimal.
Kilo = 103 = 1000 in Decimal.
Kilo = 210 = 1024 in Binary.
Mega = Kilo * Kilo = (Kilo2).
  1,048,576 Binary / 1,000,000 Decimal.
  Decimal: Mega = 106 / Binary: Mega = 220.
Giga = Kilo * Mega.
20 | 1
21 | 2
22 | 4
23 | 8
.. | ..
29 | 512
210 | 1K
211 | 2K
220 | 1M
230 | 1G
240 | 1T
5.Unsigned Numbers
5.1 Unsigned Binary
Representation
5.2 Kilo-Mega-Giga
5.3 Unsigned Number
Tables

## Slide 31: 5.3 Unsigned Numbers Table
Look at this table of 16 values we need ‘4’ Bits’
to represent all possible values.
Decimal | Binary |  | Decimal | Binary
0 | 0000 |  | 8 | 1000
1 | 0001 |  | 9 | 1001
2 | 0010 |  | 10 | 1010
3 | 0011 |  | 11 | 1011
4 | 0100 |  | 12 | 1100
5 | 0101 |  | 13 | 1101
6 | 0110 |  | 14 | 1110
7 | 0111 |  | 15 | 1111
Unsigned Numbers
  Unsigned Binary
Representation
  Kilo-Mega-Giga
  Unsigned Number Table

## Slide 32: 6. Signed Numbers
6. Signed Numbers
7. Radix Complement
The Decimal number system uses ‘-‘ (minus)
  In Binary we only have two symbols 1 and 0.
But we must be able to store signed numbers in computer memory!
One possible solution - signed magnitude
00010111 = +23
sign magnitude
10010111 = -23
sign magnitude

## Slide 33: 6. Signed Numbers
What effect does this have on the size of integers a computer can use?
8 bit unsigned binary number
00000000 - 11111111
0 - 25510
8 bit signed binary number
01111111 - 11111111
+12710 - -12710
Range (2n-1 -1) to 2n-1 -1
but we have 00000000 and 10000000 Is this a problem?
33
Signed Numbers
Radix Complement

## Slide 34: 7. Radix complement
2's complement
  Variation of sign magnitude but has some very useful characteristics.
Subtraction becomes complementary addition.
Convert -ve numbers to 2's complement and then add.
  Get subtraction through adding a negative. 30 + (-30) = 0
Signed Numbers
Radix Complement

## Slide 35: 7.1 Subtraction and Two’s Complement
To create the 2’s complement of a negative number.
  Invert all '1's to '0' and '0's to '1’
  Add 1.
Each operand must have same number of bits.
Example 25 - 7
25 = 00011001
7 = 00000111
Radix Complement
  Subtraction and Two’s Complement 7.1.1Subtraction and 2’s Complement

## Slide 36: 7.1.1 Subtraction and 2’s Comp
11111000
Step 2 : add 1
11111000
+1
1's complement
11111001 -7 in 2's complement representation
First convert -7 to 2's complement
  Step 1 : form 1's complement
00000111
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers

## Slide 37: 7.1.1 Subtraction and 2’s Comp
Now add
25 = 00011001
-7 = 11111001
Ans =100010010
The binary result 000100102 is 18 in decimal
Check answer.
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers
//ignore the carry bit if overflow occurs

## Slide 38: 7.1.1 Subtraction and 2’s Comp
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers
Another Example 7-25
25 = 00011001
7 = 00000111
First convert -25 to 2's complement
  Step 1 : form 1's complement
00011001
11100110
1's complement
Step 2 : add 1
11100110
+1
11100111 -25 in 2's complement representation
38

## Slide 39: 7.1.1 Subtraction and 2’s Comp
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers
Now add
7 = 00000111
-25 = 11100111
Ans = 11101110
The binary result is 111011102, which is a negative number (since the most significant bit is 1).
To find the magnitude, take the 2's complement of 111011102​:
Invert the bits: 000100012
Add 1: 00010001+1=000100102​=18 in decimal.
Since the original result was negative, the answer is −18.
Final Answer : 7−25=−18 using 2's complement arithmetic.
39

## Slide 40: 7.1.2 2’s complement answers.
ONLY CONVERT NEGATIVE NUMBERS!
When working out the real answer of a 2’s complement sum.
  1. Look at the most significant bit.
  2. If it is a 1 then
    The answer is negative
    Change all ones to zero, all zeros to one and add one.
    Convert this to decimal and write the sign.
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers

## Slide 41: Example
Which of the following numbers are correctly converted to 8 bit 2’s complement?
8
10
  Subtraction and Two’s Complement
    Subtraction and 2’s Complement
7.1.2 2’s complement answers Example
-3310 = 000111112
-30 = 10011000
30 = 00011110
I really don’t know

## Slide 42: 7.2 2’s Comp and Sign Magnitude
Binary | S/M | 2's Comp
00000000 | 0 | 0
00000001 | 1 | 1
00000010 | 2 | 2
····· | ····· | ·····
01111110 | 126 | 126
01111111 | 127 | 127
10000000 | -0 | -128
10000001 | -1 | -127
····· | ····· | ·····
11111110 | -126 | -2
11111111 | -127 | -1
7.2 2’s Comp and Sign Magnitude

## Slide 43: 7.2 2‘s Comp and Sign Magnitude
Number range for the sign magnitude representation for 8 and 16 bit integers?
-127 to +127
-32767 to +32767
8 bit
16 bit
Range -(2n-1 -1) to + 2n-1 -1
Number range for 2's complement 8 and 16 bit integers?
8 bit
16 bit
-128 to +127
-32768 to +32767
Range -(2n-1) to + 2n-1 -1
7.2 2’s Comp and Sign Magnitude

## Slide 44: 8. Hexadecimal (Hex)
Hexadecimal (Hex) number system is base 16.
16 unique symbols.
Symbols: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F.
10 10 10
Hexadecimal
(Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans
D = 1310, E = 1410, F = 1510.
Example: 3E816 = 100010.
A = 10 , B = 11 , C = 12 ,

## Slide 45: 8. Hexadecimal (Hex)
Weight is 16 raised to the power of the position.
Example: A1F16
(A x 162) + | (1 x 161) + | (F x 160) | 
162= 256 | 16 | 1 | 
10 x 256 + | 1 x 16 | 15 x 1 | =259110
Hexadecimal (Hex)
  Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans

## Slide 46: 8.1 Conversion of Hexadecimal to/from Decimal
Hex 9AC16
(9 * 162)+ (A * 161) + (C * 160) = 2476
2304 + 160 + 12 = 2476
1371
10
Result = 55B16
Divisor | Quotient | Remainder
16 | 1371 | 11 =B
16 | 85 | 5
16 | 5 | 5
 | 0 | 
Hexadecimal
(Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans

## Slide 47: 8.2 Binary to Hexadecimal Conversion
Comparison of the binary and hexadecimal number systems.
What do you notice?
Hexadecimal
(Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans

## Slide 48: 8.2 Binary to Hexadecimal Conversion
A single Hex digit can represent a 4-bit binary number.
Example: (110101111)
2
0001 | 1010 | 1111
1 | A | F
(110101111)2
= (1AF)16
Hexadecimal
(Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans

## Slide 49: 8.3 Binary & Hex Conversion
Consider the value:
Split this into groupings of 4 Bits
This gives the Hex – 5B16
  Hex is simply groupings of 4 Binary Bits.
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
Hexadecimal
(Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary easier for Humans

## Slide 50: 8.4 Making Binary Easier for Humans
Why was Hexadecimal chosen?
  Single hex digit = four bits.
  2 hex digits per byte.
  Allows simple conversion to and from binary.
  Simpler to convert between Base 2 and Base 10.
  The meaning of a value can be communicated simply and effectively, both at the computer (i.e. Base 2) level and also so that humans (i.e. Base 10) can visualise the meaning.
    Hex is easier for humans to understand and communicate.
    Example: A16 = 10102 = 1010.
Hexadecimal (Hex)
  Conversion of Hexadecimal to/from Decimal
  Binary to Hexadecimal Conversion
  Binary &Hex Conversion
  Making Binary
easier for Humans

## Slide 51: 9. OCTAL Radix 8
The only other commonly used number base is 8 or Octal.
Why use octal?
  Direct conversion to binary
How would you represent 23 decimal in octal?
  Hint 2310 is 000101112 in 8 bit binary.
  The answer is : 027
OCTAL Radix 8
Non Integer Numbers

## Slide 52: 10. Non Integer Numbers
Can we always use WHOLE values?
It would be nice if we could.
  Bank balances might be interesting.
  We need to look at what are called Floating Point numbers.
Values such as 3.142, etc.
  Numbers with a decimal point!
  Data types such as double (in Java and C).
OCTAL Radix 8
Non Integer Numbers

## Slide 53: 10.1 Scientific Notation
This is a way of expressing very large and very small numbers.
537,000,000 is written 5.37 x 108
  5.37 is called the Mantissa.
  108 is called the Exponent.
0.000136 is written 1.36 x 10─4
  1.36 is called the Mantissa.
  10─4 is called the Exponent.
Non Integer
Numbers
  Scientific Notation
  Scientific Notation: Floating Point Numbers

## Slide 54: 10.2 Scientific Notation: Floating Point Numbers
Note that a positive exponent tells you how many places to move the decimal point to the right, making the number. bigger.
A negative Exponent is how many places to move the decimal point to the left, making the number smaller.
1.005 x 100 = 1.005 1.005 x 104 = 10,050
These are called Floating Point numbers.
1.005 x 102 = 100.5
1.005 x 10-2
= 0.01005
10.1 Scientific
Notation
10.2 Scientific
Notation: Floating
Point Numbers
10.3 Binary:
Floating Point
Format
10.4 Floating Point
in Decimal

## Slide 55: 10.3 Binary: Floating Point Format
Expressing a number as a Mantissa and an Exponent allows us to store Floating Point numbers in a format that only requires whole numbers.
Sign = 1 bit.
Mantissa = 7 bits.
Exponent = 8 bit signed magnitude.
Total = 16 bits.
5.62510
+101.10102
1.011010 x 22
  Scientific Notation: Floating Point Numbers
  Binary: Floating Point Format
  Floating Point in Decimal
  Floating
Point in Binary

## Slide 56: 10.4 Floating Point in Decimal
100 | Point | 10-1 | 10-2 | 10-3
1 |  | 1/10 | 1/100 | 1/1000
3 | . | 1 | 4 | 2
What does 3.14210 actually mean?
3.142 = (3 * 1) + (1 * 1/10) + (1 * 4/100) + (1 * 2/1000)
= 3 + 0.1 + 0.04 + 0.002
  Binary: Floating Point Format
  Floating Point in Decimal
  Floating
Point in Binary

## Slide 57: 10.5 Floating Point in Binary
What is 1.1012?
1.1012 = (1 * 1) + (1 * 1/2) + 0 + (1 * 1/8)
1 + 0.5 + 0 + 0.125
= 1.62510
20 | Point | 2-1 | 2-2 | 2-3
1 |  | 1/2 | 1/4 | 1/8
1 | . | 1 | 0 | 1
  Floating Point in Decimal
  Floating
Point in Binary
  Limitation in Binary
  Converting
Decimal to Binary

## Slide 58: 10.6 Limitation in Binary
The Columns as we go RIGHT after the POINT have the place values.
When converting Floating Point decimal numbers to binary using a fixed number of places.
NOT ALL VALUES ARE POSSIBLE!
1/2 | 1/4 | 1/8 | 1/16 | 1/32
0.5 | 0.25 | 0.125 | 0.0625 | 0.03125
  Floating Point in Decimal
  Floating
Point in Binary
  Limitation in Binary
  Converting
Decimal to Binary

## Slide 59: 10.7 Converting Decimal to Binary
Use continuous multiplication by 2.
Each 1 or 0 to the left of the point of the result contributes to the binary number.
Continue until the fractional part is 0.
Or until you obtain the answer to the accuracy you need.
  Binary: Floating Point Format
  Floating
Point in Decimal
  Floating Point in Binary
  Limitation in Binary
  Converting Decimal to Binary

## Slide 60: 10.7.1 Example: Decimal to Binary
Take the Decimal Fraction: 0.35
0.35 | x | 2 | 0.70 | 0
0.70 | x | 2 | 1.4 | 1
0.4 | x | 2 | 0.8 | 0
0.8 | x | 2 | 1.6 | 1
0.6 | x | 2 | 1.2 | 1
0.2 | x | 2 | 0.4 | 0
Answer: | 0.35 = | 0.01011 | ...and so on | 
MSB
LSB
  Converting Decimal to Binary
    Example: Decimal to Binary
    How close is this answer to 0.35?

## Slide 61: 10.7.2 How close is this answer to 0.35?
0.0101102
20 |  | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
0 | . | 0 | 1 | 0 | 1 | 1 | 0
0*20 | 0
1* 2-2 = 1* 0.25 | 0.25
1* 2-4 = 1* 0.0625 | 0.0625
1* 2-5 = 1* 0.0625 | 0.03125
 | 0.34375
    Example: Decimal to Binary
    How close is this answer to 0.35?
10.8 Accuracy of Floating Point Data

## Slide 62: 10.8 Accuracy of Floating Point Data
Accuracy defined as closeness to true value.
Data is inputted to a program in Decimal floating point format (e.g. via the keyboard).
It is converted to a binary floating point format of fixed size.
This may involve some loss of accuracy.
Floating Point arithmetic is only approximate.
Integer arithmetic is exact.
    Example: Decimal to Binary
    How close is this answer to 0.35?
10.8 Accuracy of Floating Point Data

## Slide 63: 10 Storage Needs
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic
63

## Slide 64: 11.1 Precision
Determined by the number of bits used to store the
Mantissa.
A high precision format will result in more accurate floating point arithmetic.
Most languages provide a choice:
  Single precision.
  Double precision.
64
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic

## Slide 65: 10.2 Range
The range of the format is how big and how small the numbers are that can be represented.
Determined by the number of bits used for the Exponent.
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic
65

## Slide 66: 11.3 Formats That have been used
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic

## Slide 67: 11.4 IEEE Format now Used
IEEE 754 floating point standard.
Single Precision (32 bits):
  Mantissa:
    1 Bit for Sign / 23 Bits for Value.
  Exponent:
    8 Bits.
Double Precision (64 bits):
  Mantissa:
    1 Bit for Sign / 52 Bits for Value.
  Exponent:
    11 Bits.
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic

## Slide 68: 10.5 Floating Point Arithmetic
Manipulating Floating Point numbers to do arithmetic is more complex than with Integer arithmetic.
Early processors only did Integer arithmetic – FP arithmetic was done in software.
Then math co-processors were introduced to do Floating Point calculations.
Now, most processors implement Floating Point instructions.
10. Storage Needs
10.1. Precision
10.2. Range
10.3. Formats that have
been used
10.4. IEEE Format now
Used
10.5. Floating Point
Arithmetic
68

## Slide 69: 12. Summary
Representation of Numbers
Base/Radix: Hex and Octal
Non-integer numbers and Floating Point numbers.
  IEEE Format
now used
  Floating Point Arithmetic 12.Summary