## Slide 1
Lecture 2: 4CS015
1
Digital Electronics

## Slide 2
A.Coverage
  Boolean Logic and Logic Gates
    Truth Table
  Boolean Algebra Laws
  Combinational Circuit
2
A.Coverage
1. Boolean Logic
1.1 Basic Definitions

## Slide 3: 1. Boolean Logic History
3
George Boole (1815-1864)
  “An Investigation into the Laws of Thought”
  Defined an algebra for solving logical problems
  Limited to dealing with facts True or False
  Now known as Boolean Algebra
1. Boolean Logic History
1.1 Basic Definitions

## Slide 4: 1.1 Basic Logic Definitions
4
In a Logic System a variable can have one of two possible states.
Single capital letters are used to represent variables.
The bits 1 and 0 are also used as constants.
TRUE | ON | CLOSED | ‘1’ | Yes | 5v
FALSE | OFF | OPEN | ‘0’ | No | 1v
1. Boolean Logic
1.1 Basic Definitions
1.2 Logic States

## Slide 5: 1.2 Logic States
5
If a switch is closed:
  The light will be ON.
  This can represent Logic TRUE.
If a switch is open:
  The light will be OFF.
  This can represent Logic FALSE.
The switch is a Logic variable.
1. Boolean Logic
1.1 Basic Definitions
1.2 Logic States
2. Boolean Operators

## Slide 6: 2. Boolean Operators
6
Boole defined three basic operations that could be used with these Boolean variables.
    AND
    OR
    NOT
All logical expressions can be built from these three.
2. Boolean Operators

## Slide 7: 2. Boolean Operators
7
Logical AND
Logical OR
Logical NOT
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.3 Logical NOT

## Slide 8: 2.1 Logical AND
8
How can we switch the light on?
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.3 Logical NOT

## Slide 9: 2.1 Logical AND
9
Boolean Expression:
F = A AND B or F= A∙B
Gate Diagram:
A B
F
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table:
2. Boolean Operators
2.1 Logical AND
2.1.1 AND Relationship 2.2 Logical OR
2.3 Logical NOT

## Slide 10: 2.1.1 AND Relationship
10
Boolean representation . (Period)
If F,A and B are Boolean variables.
Then the expression F = A∙B means
  F is only true when A AND B are both true.
As A is capable of being 1 or 0 and B is capable of being 1 or 0 there are 4 possible states. 00, 01, 10 or 11
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
2. Boolean Operators
2.1 Logical AND
2.1.1 AND Relationship 2.2 Logical OR
2.3 Logical NOT

## Slide 11: 2.2 Logical OR
11
Battery
Switch A
Switch B
Light
How can we switch on the light?
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.3 Logical NOT

## Slide 12: 2.2 Logical OR
12
Boolean Expression:
F = A OR B alternatively F =A+B
Gate Diagram:
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table:
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.2.1 OR Relationship
2.3 Logical NOT

## Slide 13: 2.2.1 OR Relationship
13
Boolean representation + (Plus)
If F,A and B are Boolean variables.
Then the expression F = A+B means
  F is only true when A OR B, OR both, are true.
As A is capable of being 1 or 0 and B is capable of being 1 or 0 there are 4 possible states. 00, 01, 10 or 11
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.2.1 OR Relationship
2.3 Logical NOT

## Slide 14: 2.3 Logical Not
14
Battery
Switch A
Light
How can we switch the light off?
Boolean Expression:
F = NOT A or F=!A or F=A’
A
F
Gate Diagram:
Input A | Output F
0 | 1
1 | 0
Truth Table:
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.3 Logical NOT
2.3.1 NOT Relationship

## Slide 15: 2.3.1 NOT Relationship
15
The NOT relationship reverses the value.
NOT True is False etc…
The Symbol ( ) used is usually a bar above the variable or expression to be reversed
E.g if A= true then A’ = false
In some circumstances we use !
E.g. if B = true !B = false (easier to type)
2. Boolean Operators
2.1 Logical AND
2.2 Logical OR
2.3 Logical NOT
2.3.1 NOT Relationship
3. Integrated Circuit and Logic gates

## Slide 16: 3. Integrated Circuit and Logic Gates
16
3. Integrated Circuit and Logic gates

## Slide 17: 4. Other Logic Gates
To make life a little easier the basic logical functions are expanded to include:
  NAND
    This is an AND with a NOT output.
  NOR
    This is an OR with a NOT output.
  XOR
    This is the Exclusive OR function.
  XNOR
    This is Complement of XOR.
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR

## Slide 18: 4.1 NAND
Truth Table:
Boolean Expression:
F = NOT(A AND B) F = A∙B
Gate Diagram:
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR
A | B | A.B | 
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | A.B | 
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 19: 4.2 NOR
Truth Table:
Boolean Expression:
F = NOT(A OR B) , F = A+B
Gate Diagram:
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR
A | B | A+B | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | A+B | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 20: 4.3 XOR
Truth Table:
generates low output when both the inputs are either low 0or high 1.
Boolean Expression:
F = A XOR B or F = A⊕B
Gate Diagram:
A B
F
Input A | Input B | Output F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR

## Slide 21: 4.4 XNOR
Truth Table:
generates high output when both the inputs are either low 0 or high 1.
Boolean Expression:
F = A XNOR B or F = A ☉ B
Gate Diagram:
Input A | Input B | Output F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR
5. Boolean Algebra laws

## Slide 22: 5. Boolean Algebra Laws
The operations +, . And ’ consequently satisfy the basic laws 1, 2 and 3 of Boolean algebra. That is:
A + B ≡ B + A
A ⋅ B ≡ B ⋅ A
Commutative Laws
(A + B) + C ≡ A + (B + C)
(A ⋅ B) ⋅ C ≡ A ⋅ (B ⋅ C)
Associative Laws
A ⋅ (B + C) ≡ (A ⋅ B) + (A ⋅ C)
A + (B ⋅ C) ≡ (A + B) ⋅ (A + C)
Distributive Laws
4. Other Logic Gates
4.1 NAND
4.2 NOR
4.3 XOR
4.4 XNOR
5. Boolean Algebra laws

## Slide 23: 5. Boolean Algebra Laws
Identity Law Negation Law
A + 0 = A low = high
A . 1 = A ( 0 = 1 )
Idempotent Law
A + A = A
A . A = A
Complement Law
A . A’ = 0
A + A’ = 1
Double Negation Law
A = A
Domination Law
A + high = high A . low = low
(A + 1 = 1) A . 0 =0
Absorption Law
A + (A .B) = A
A . (A + B) = A
5. Boolean Algebra laws

## Slide 24: 5.1 DeMorgan’s Laws
A+B = A .B
5. Boolean Algebra laws
5.1 DeMorgan’s Laws
6. Universal Gate
De Morgan’s 1st Law: “The complement of a sum is equal to the product of the complements”
A | B | A+B |  |  |  | .
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0
A | B | A+B |  |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 25: 5.1 DeMorgan’s Laws
A.B = A+.B
5. Boolean Algebra laws
5.1 DeMorgan’s Laws
6. Universal Gate
De Morgan’s 2nd Law: “The complement of a product is equal to the sum of the complements”
A | B | A.B |  |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0
A | B | A.B |  |  |  | 
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 26
The repeated use of a NOR or a NAND gate alone can produce all the three basic logic gates.
Universal Gate
5. Boolean Algebra laws
5.1 DeMorgan’s Laws
6. Universal Gate

## Slide 27
Question 1 : NAND and NOR gates are called universal gates, why?
6. Universal Gate
6.1 AOI Using NAND gate
6.2 AOI Using NOR gate

## Slide 28
AOI using NAND and NOR gate
AOI using NOR gate?
6. Universal Gate
6.1 AOI Using NAND gate
6.2 AOI Using NOR gate
7. Precedence of operators
Logic Function Only
Symbol
Circuit Using NAND gate
NOT
AND
OR

## Slide 29
AOI using NAND and NOR gate
6. Universal Gate
6.1 AOI Using NAND gate
6.2 AOI Using NOR gate
7. Precedence of operators
Logic Function Only
Symbol
Circuit Using NOR gate
NOT
AND
OR

## Slide 30
7. Precedence of operators
As with normal mathematics when working out the value of a function it is very important to do it in the right order.
NOT AND OR
Parenthesis (brackets) override in the normal way.
When a bar goes above more than 1 symbol it becomes a bracket that reverses.
6. Universal Gate
6.1 AOI Using NAND gate
6.2 AOI Using NOR gate
7. Precedence of operators

## Slide 31
7.1 Example
7. Precedence of operators
7.1 Example
8. Circuit Design

## Slide 32
8. Circuit Design
7. Precedence of operators
7.1 Example
8. Circuit Design

## Slide 33
8.1 Digital Component
The main thing to remember is that combinations of gates implement Boolean functions.
The circuit below implements the Boolean function:
We simplify our Boolean expressions so that we can create simpler circuits.
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic

## Slide 34
8.2 Truth Table
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic

## Slide 35
8.3 Combinational Logic
We have designed a circuit that implements the Boolean function:
This circuit is an example of a combinational logic
circuit.
Combinational logic circuits produce a specified output (almost) at the instant when input values are applied.
  In a later section, we will explore circuits where this is not the case.
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic

## Slide 36
8.3.1 Combinational Circuit Examples
Example 1
Circuit after Simplification
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples

## Slide 37
Example 2
8.3.1 Combinational Circuit Examples
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples

## Slide 38
Example
Simplify:
X = (A.B.C) +(A.B'.C) +(A'.B.C)
8.3.1 Combinational Circuit Examples
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples

## Slide 39
Example 4: Write the output functions of the following circuits.
8.3.1 Combinational Circuit Examples
Fig: Multiplexor
Fig: Decoder
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples
8.3.2 Exercises

## Slide 40
Exercises
Simplify and construct the logic circuit:
A’.B’ + (A.B)’
(A + B).(A + B) + A.(A + B’)
(A.B’.C’ + A’.B’.C+A.B.C+A’.B.C’)
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples
8.3.2 Exercises
9. Summary

## Slide 41
9. Summary
41
We have looked at the basic logic gates:
  Identifying OR, AND, NOT, NAND, NOR and XOR.
We have seen that gates can be joined together to form Combinatorial Logic.
8. Circuit Design
8.1 Digital component
8.2 Truth table
8.3 Combinational Logic
8.3.1 Examples
8.3.2 Exercises
9. Summary

## Slide 42
42
Thank you…