## Slide 1: 4CS015 Lecture 3: Combinational Circuit

## Slide 2: 1. Lecture 3 coverage
Review of Week 2
  Boolean gates and logic
Mathematical functions in logic!
  Understanding addition
  Making our own truth tables
  Building a circuit that can perform maths
  Reducing logic
1. Lecture 3 coverage

## Slide 3: 2. Boolean Expression Reduction
2. Boolean Expression Reduction
2.1. Boolean Expression
from Truth table
2.1.1. SOP Expression from
Truth table
2.1.2. SOP Expression from
Truth table

## Slide 4: 2.1. Boolean Expression from Truth table
How do we derive Boolean Expression from the given Truth Table??
SUM OF PRODUCT
  SOP Expression:
  F = A’BC + AB’C + ABC’+ABC
PRODUCT OF SUM
  POS Expression:
F = (A + B + C) (A + B + C ‘) (A + B’ + C) (A’ + B + C)
How do we know?? Well we will know that today.
2. Boolean Expression Reduction
2.1. Boolean Expression
from Truth table
2.1.1. SOP Expression from
Truth table
2.1.2. SOP Expression from
Truth table

## Slide 5: 2.1.1. SOP Expression from Truth table
SUM OF PRODUCT
Scan for 1 in output variable (F)
Scan its corresponding input variable,
  Here, A = 0 , B = 1 and C= 1
If input is “1” write the variable as it is and if the variable is “0” then complement the variable. AND the variable together.
  The first expression is A’.B.C
Do likewise for all the remaining output then OR the AND terms to obtain the output function.
  F = A’BC + AB’C + ABC’+ABC
2. Boolean Expression Reduction
2.1. Boolean Expression
from Truth table
2.1.1. SOP Expression from
Truth table
2.1.2. SOP Expression from
Truth table

## Slide 6: 2.1.2. POS Expression from Truth table
PRODUCT OF SUM
Scan for 0 in output variable (F)
Scan its corresponding input variable,
  Here, A = 0 , B = 0 and C= 0
If input is “0” write the variable as it is and if the variable is “1” then complement the variable. OR the variable together.
  The first expression is A+B+C
Do likewise for all the remaining output then AND the Or terms to obtain the output function.
  F = (A + B + C) (A + B + C ‘) (A + B’ + C) (A’ + B + C)
2. Boolean Expression Reduction
2.1. Boolean Expression
from Truth table
2.1.1. SOP Expression from
Truth table
2.1.2. POS Expression from
Truth table

## Slide 7: 3. Circuit Design
Three Steps starting from given circuit requirements in the form of a table.
Formulate a Boolean expression for the output function from the given table Using SOP or POS expression.
Simplify this expression as much as possible using Boolean algebra.
Draw the circuit corresponding to the simplified output function.
3. Circuit Design (Contd.):

## Slide 8: 3. Circuit Design (Contd.):
Example:
We will design a circuit corresponding to the following truth table. The output function is labelled X.
3. Circuit Design (Contd.):

## Slide 9: 3. Circuit Design (Contd.):
Step 1. First scan the output column for occurrences of 1. In this example there are three (lines 1, 2 and 4).
For each of these lines construct a sub-expression involving A and B and the operations AND (⋅) and NOT ( ͞ ) only that will return the value 1 for the corresponding input values.
In row 1, A = 1 and B = 1 so A ⋅ B will return the value 1 for these input values and for no others.
3. Circuit Design (Contd.):

## Slide 10
In row 2, A = 1 and B = 0 so A ⋅ B will return the required 1 for these values
Finally, with A = 0 and B = 0, row 4 will require A ⋅ B
The three expression obtained are then combined together using OR (+) operations. The final expression
3. Circuit Design (Contd.):
3. Circuit Design (Contd.):

## Slide 11: 3. Circuit Design (Contd.):
Step 2: Simplify the Boolean Expression.
3. Circuit Design (Contd.):

## Slide 12: 3. Circuit Design (Contd.):
Step 3: The circuit for the simplified output function X requires
only two gates:
Check that the truth table for X = A + B agrees with the original.
The method extends easily to three or more input pulses.
3. Circuit Design (Contd.):

## Slide 13
Another Example:
Design a Circuit corresponding to:
A | B | C | X
1 | 1 | 1 | 1
1 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 0 | 0 | 0
0 | 1 | 1 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 0
3. Circuit Design (Contd.):
3. Circuit Design (Contd.):

## Slide 14
Step 1 There is a 1 in lines 1, 3 and 5 of the output column.
The sub-expressions which will return 1 in these lines are, respectively
A ⋅ B ⋅ C, A ⋅ B ⋅ C and A ⋅ B ⋅ C
The Boolean Expression is therefore given by
X = (A ⋅ B ⋅ C) + (A ⋅ B ⋅ C) + (A ⋅ B ⋅C)
3. Circuit Design (Contd.):
3. Circuit Design (Contd.):

## Slide 15
Step 2 : Simplify
The simplified Boolean Expression is therefore given by
X = (A ⋅ B ⋅ C) + (A ⋅ B ⋅ C) + (A ⋅ B ⋅ C)
X = (A ⋅ B ⋅ C) + (A ⋅ B ⋅ C) + (A ⋅ B ⋅ C)
X = A.C (B + B ) + (A ⋅ B ⋅ C)
X = A.C .1 + (A ⋅ B ⋅ C) (Complement law)
X = A.C + (A ⋅ B ⋅ C)
X = C . ( A + A . B)
X = C . (A + B) (Distributive law)
X = C . (A + B)
3. Circuit Design (Contd.):
3. Circuit Design (Contd.):

## Slide 16
Step 3 The circuit for (A + B) ⋅ C is
3. Circuit Design (Contd.):
3. Circuit Design (Contd.):

## Slide 17: 4. Exercises ……
1.Design a Circuit corresponding to following truth tables:
A | B | C | X
1 | 1 | 1 | 1
1 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 0 | 0 | 0
0 | 1 | 1 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
0 | 0 | 0 | 1
A | B | C | X
1 | 1 | 1 | 0
1 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 0 | 0 | 0
0 | 1 | 1 | 1
0 | 1 | 0 | 1
0 | 0 | 1 | 1
0 | 0 | 0 | 0
4. Exercises ……

## Slide 18: 4. Exercises ……
Simplify and construct the logic circuit:
A’.B’ + (A.B)’
(A + B).(A + B) + A.(A + B’)
(A’. B + A.B’)’
((A + C).(AB)’ + (BC + A’)’)’
(A.B’.C’ + A’.B’.C+A.B.C+A’.B.C’)
4. Exercises ……

## Slide 19: 5. Addition Rules as a Table
Number 1 and Number 2 are the Inputs.
Sum and Carry are the results after addition.
Number 1 | Number 2 | Result | Carry Over
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
5. Addition Rules as a Table

## Slide 20: 6. Addition as Logical Functions
Assume that SUM is now a truth table Entry then:
Doing the same for CARRY we get:
Input A Number 1 | Input B Number 2 | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
6. Addition as Logical Functions

## Slide 21: 7. Half Adder
Combinational logic circuits give us many useful devices.
One of the simplest is the half adder, which finds the sum of two bits.
We can gain some insight as to the construction of a half adder by looking at its truth table, shown at the right.
7. Half Adder

## Slide 22
Input A | Input B | S (Sum) | C (Carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
7. Half Adder
7. Half Adder

## Slide 23
Input A | Input B | Carry IN | Sum | Carry OUT
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
8. Full Adder function
8. Full Adder Function
8.1 Full Adder
8.2 Full Adder from Two Half
Adders
8.3 Symbol for a Full Adder

## Slide 24
We could derive the full Boolean expression for the Sum and Carry OUT.
However, there is a great deal of symmetry associated with the half and full adder and we can simply build a FULL from two Halves.
8.1 Full Adder
8. Full Adder Function
8.1 Full Adder
8.2 Full Adder from Two Half
Adders
8.3 Symbol for a Full Adder

## Slide 25: 8.2 Full Adder from Two Half Adders
The Full Adder:
The Half Adder
 |  | 1 | 1 | 0
+ |  | 1 | 1 | 1
carry: | 1 | 1 | 0 | 
 | 1 | 1 | 0 | 1
8. Full Adder Function
8.1 Full Adder
8.2 Full Adder from Two Half
Adders
8.3 Symbol for a Full Adder

## Slide 26: 8.3 Symbol for a Full Adder
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
8. Full Adder Function
8.1 Full Adder
8.2 Full Adder from Two Half
Adders
8.3 Symbol for a Full Adder

## Slide 27: 9. Reduction.
If you develop the sum of products for the full adder.
Sum = ABC+ABC+ABC+ABC
Carry OUT = ABC+ABC+ABC+ABC
These show very little resemblance to the circuits we are using.
By applying the laws and theorems of Boolean algebra we should be able to get from the above to our circuits.
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
9. Reduction:
9.1. Reduction Basics
9.2. Reduction Example

## Slide 28: 9.1 Reduction Basics
AND relationship
0.X = 0
1.X = X
X.X = X
X.X = 0
OR relationship
0+X = X
1+X = 1
X+X = X
X+X = 1
Not
X = X
Theorem
(X+Y)(X+Y) = X
because
(X+Y)(X+Y) = X.(Y+Y)
and Y+Y = 1
and X.1 = X
9. Reduction:
9.1. Reduction Basics
9.2. Reduction Example

## Slide 29: 9.2 Reduction Example
X
Y
Z
X.Y + X.Z
X
Y
Z
X.(Y+Z)
As the outputs are same for all inputs we can use this to reduce XY+XZ
To X(Y+Z)
Absorption
9. Reduction:
9.1. Reduction Basics
9.2. Reduction Example

## Slide 30: 9.2 Reduction Example
X
(X)
Always on
So X+X= 1
1 = always on
X
Y
Y
X.Y + X.Y
X
=Y
9. Reduction:
9.1. Reduction Basics
9.2. Reduction Example

## Slide 31: 10. Carry: Sum of Products
Carry = ABC+ABC+ABC+ABC
Carry = ABC+ABC+ABC+ABC+ABC+ABC
BC(A+A)
AC(B+B)
AB(C+C)
Carry = A.B+B.C+A.C
We have simply
applied Theorem 6
3 times.
10. Carry: Sum of Products

## Slide 32
Sum = ABC+ABC+ABC+ABC
1. Sum =A(BC+BC)+A (BC+BC)
2. BC+BC = B C
3. BC+BC = B C
4. Substitute X for B C
5. We get AX + AX
6. A X
7 substitute B C = X
8. Sum = A (B C)
10. Sum: Sum of Products
10. Sum: Sum of Products

## Slide 33: Summary
We have looked at the basic logic gates:
  Identifying OR, AND, NOT, NAND, NOR and XOR.
We have seen that gates can be joined together to form Combinatorial Logic.
summary